Music Generation and Sound Processing in a Functional Programming Paradigm
Giorgi Botkoveli
Cenikj Nikola
Abdin Hossameldin
Beka Grdzelishvili
Le Minh Nghia
Evan Sitt
Sylaj Tringa
Su Xiaotian
Szumi Xie
Ying Xue
Viktória Zsók
Tsinadze Zurab

---
Digital Synthesis
Digital Synthesis
- First pioneered in 1957 with a punch card controlled analog synthesizer using 750 vacuum tubes.
- Popularized in the music of the 1980’s by the Yamaha DX7
- Extensively popular today across many disciplines.
  - Music
  - Telecommunications
  - Speech Translation

---
Additive Synthesis
Additive Synthesis
- Summation of input wave signals to create a new output signal.
- Synthesizing a Fourier series by weighted summation of harmonics of the basic sine wave can generate all waves imaginable.
- Limited only by processing power.
- Resulting waveforms can be stored into waveform tables.

---
Wavetable Lookup Synthesis
Wavetable Lookup Synthesis
Waveform values stored into a lookup table.
  - Typically a single period is stored.
  - Can store complex waveforms.
- Ease of access based on frequency.
- Faster and more efficient synthesis method.

---
ADSR Envelope
ADSR Envelope
Applies dampening/expansion to different stages of a sound.
  - Attack - Modifies sound from 0 to max amplitude from noteOn.
  - Decay - Modifies sound from max amplitude to Sustain level after Attack phase.
  - Sustain - Level of max amplitude to hold constant after Decay phase.
  - Release - Modifies sound from Sustain level to 0 after noteOff.
- Drastically alters a sound’s character.
- Can be extended to a DAHDSR Envelope.

---
MIDI
MIDI
Stands for “Musical Instrument Digital Interface”
  - “Technical standard that describes a communications protocol, digital interface, and electrical connectors that connect a wide variety of electronic musical instruments, computers, and related audio devices for playing, editing and recording music.”
- Contains detailed instructions that can be interpreted into musical notation.
- Can further contain other detailed information for synthesizer standards such as General MIDI (GM)

---
Waveform Audio File Format
Waveform Audio File Format
An audio file format standard, developed by Microsoft and IBM, for storing an audio bitstream on PCs.
  - Resource Interchange File Format (RIFF) bitstream format
  - Pulse Code Modulation (PCM) Encoding
  - Uncompressed, universally supported.

---
Applications
Applications
- Music and Sound Generation
- Text to Speech
- Digital Signal Processing
- Telecommunications
- Many more...

---
Thank you for your attention!
Thank you for your attention!